## Slide 1: CYBER SECURITY UPSKILLING PROGRAM قدم خلال مبادرة زنك/2 في جامعة البلقاء التطبيقية بالتعاون مع أكاديمية سايبر شيلد AUG 2024 Networks Part Version 1
INST.:ENG.ALI BANI BAKAR-0778642376(CYBER SHIELD ACADEMY)
DONE BY: ENG. Dana Al-Mahrouk-0798697842-BAU.UNIV.

## Slide 2: Outline
Networks
Linux Essentials
Cybersecurity Foundation
Ethical Hacking
Digital Forensic Investigation

## Slide 3: Networking
TCP/IP & OSI Model
Network Devices
Host Devices
Tool:
  Packet Tracer
  Wireshark
  GNS3

## Slide 4: Day 1
Outline:
  TCP/IP Model
  Network Devices
    Switch
    Router
  Host Devices
    PC
    Server
      Web Server
      DNS Server
  Message & Ping
  Broadcast & ARP Table
  Project at packet tracer

## Slide 5: TCP/IP Model
Have 5 Layers
From CISCO
Encapsulation:
Each layer adds its own data [control data] to the [Data].
Data
[Transport Header (Port #) | Data]  Segment
[Network Header (IP) | Port # | Data]  Packet
[Data Link Header (MAC) | IP | Port # | Data]  Frame
Bits

## Slide 6: Network Devices
Switch:
Connects between two host devices (End devices), one Network.
Work at layer 2 (Data Link Layer)  MAC Address.
Switch have ports:
Console
Fast Ethernet [0/1 – 0/24 || 0/32]
Gigabit Ethernet [0/1 – 0/2]

## Slide 7: Message
Test connection: (Ping)  ICMP ‘L3 Network ’
  Echo request
  Echo replay / response
Add message  Error  PC has no functional ports  PC need IP Address
Solution  PC  Desktop  IP Configuration :
  IPv4 Address: 192.168.0.2 ~ 192.168.0.4
  Subnet Mask: 255.255.255.0  Default no change
Q: Switch works at layer 2 (Data link), it can see the MAC Address only (can not see the IP Address), ‘MAC Address is a unique number comes with the device when you bought it’, the question is: Why does the connection succussed only when we put IP Address –layer 3 (Network)- to PC?

## Slide 8
1) Send message  ping
2)
Request:
[src MAC | dest MAC | src IP | dest IP | Data]
[ 02 | ?? | .0.2 | .0.3 | Data]
Sender does not know the MAC Address for Destination
Q: How can switch solve that?
A: By using Broadcast
Note:
Switch has a Table that contains MAC | Port #
 called MAC Table, Switch Table
B) Broadcast MAC  FF:FF:FF:FF:FF:FF
Switch sends the message to all devices (except sender), to identify the MAC Address of the Destination IP Address that sender needs to know.
Note:
Broadcast IP  255.255.255.255
A) Ping <dest / target ip>
C) Only the PC that has that dest IP will receive a message (that contain the IP Address for that PC)  Uni-cast
Note:
Sender will save the IP MAC Address for that Receiver at ARP Table
MAC | Port #
02 | FE 0/1
03 | FE 0/2
04 | FE 0/3
arp -a
Replay:
[src MAC | dest MAC | src IP | dest IP | Data]
[ 03 | 02 | .0.3 | .0.2 | Data]
Broadcast message
ARP L2
F0/1
F0/2
F0/3

## Slide 9
Ping message
ICMP L3
sender
receiver
Echo Request
Echo Reply
A) The sender sends the message to the switch, after searching for the MAC address and extracting it from the ARP Table for PC0.
B) The switch works on the L2, Data Link Layer, which depends on the MAC address of the sender and receiver.
The switch cannot see the layers above the second layer, so if the sender does not have the recipient's MAC address, the switch sends a Broadcast message.
C) The message reaches the destination successfully; The receiver sends a replay message to the sender to confirm that the message has arrived successfully.
- The computer can deal with all network layers, so the computer receiving the message can open the message and read the data.
- If there is no computer with the IP address to which the sender wanted to send the message, it will be returned Request Time Out from switch.
D & E) The switch sends this message to the sender, and it reaches the computer successfully
Q: ICMP use TCP or UDP protocol?
Not one of them. ICMP is a protocol in L3, the network layer, and TCP and UDP are in L4, the transport layer. Protocols in a specific layer use protocols in the layer below them.
E
D
C
A
B
IP | MAC
.0.2 | 03
.0.3 | 04

## Slide 10: Message Transport
IP Address
IP Address
Sender PC
Receiver PC
MAC Address
MAC Address
MAC Address
Ping ICMP

## Slide 12
*] At the beginning, there is no ARP Table, however, when PC ping starts to send messages to other PCs at first time  Broadcast sends to all PCs  Target PC receives it own MAC Address  Now, the sender PC get the MAC Address to Distance PC  it saves it at ARP Table & after that it sends message.
**] If target PC found  message [Broadcast message] + 4 echo request – replay  (4 * 2) + 2 = 10
If not found  Request Time out  [Broadcast message]  2
Note:
ARP scanner  fast and danger [Python]

## Slide 13
[192.168.0.2 192.168.0.3 192.168.0.4] [192.168.1.2]
Same Network 1
Network 2
Consider subnet mask: 255.255.255.0
Switch can connect devices that can communicate in one network
ping
Connection fail
Connection success

## Slide 14: Server
It provides service to users using specific port.
Web Server:
is a computer system capable of delivering web content to end users over the internet or intranet via a web browser
DNS server:
translates domain names into IP addresses, enabling users to access websites using names.

## Slide 15
Packet Tracer Typology (CISCO)
Give PCs IP Address.
Give Web Server IP Address
Give Web Server HTTP Service & write simple web page.
PC Connect with Web Server by IP Address
Give DNS Server IP Address & DNS Service, give Web Server a name.
Give PCs DNS Server & connect with Web Server by name

## Slide 16
A) Give PCs IP Address

## Slide 17
1
2
B) Give Web Server IP Address

## Slide 18
5
4
3
2
1
C) Give Web Server HTTP Service & write simple web page.

## Slide 19
1
4
3
2
D) PC Connect with Web Server by IP Address

## Slide 20
Q: how to connect to a web page using DNS?
A: Using DNS Server that convert name to IP Address of Web Server.

## Slide 21
E) Give DNS Server IP Address & DNS Service, give Web Server a name.

## Slide 22
F) Give PCs DNS Server & connect with Web Server by name

## Slide 23
How It Work now?

## Slide 24
1
4
3
2
Name
Name
Search in DNS Table
-------------------------
Name | IP Address
IP Address
IP Address

## Slide 25
5
8
7
6

## Slide 26: Router
Connects between two network.
PC connects to other PC on different network using Router and put Default Gateway to IP Address of the Router Interface IP that connected to switch to that network.

## Slide 27
Give PC Default Gateway

## Slide 28
Give Router IPs Address

## Slide 29: Question
Q1: How many Networks in the typology?
A: 13
Q2: Can a PC or server can be configured to act as a default gateway in a network
A: Yes, as firewall
Q3 : How many Networks?
Ans: 1

## Slide 30: Day 2
Outline:
  IPv4
  Subnetting and CIDR
  Network ID & Broadcast IP Examples
  DHCP :APIPA & DHCP Server
  How does DHCP work?
  GNS3
  Wireshark
  Exercises

## Slide 31: IPv4
MAC Address  do not care about it, it changes during message sending – transform at each router.
IPv4:
4 digit  each 8-bit 1-byte Octet
4 * 8-bit = 32-bit  2^32 = 4 billions IP Address
8-bit each  2^8 = 256  [0 - 255]
_____ . _____ . _____ . _____
IPv6:
8 digit  each 16 bit | 4 hexadicemal  128 bit
ffff:ffff:ffff:ffff:ffff:ffff:ffff:fffff
Q: why IPv4 still use? (the answer will be discussed later)
0-255
0-255
0-255
0-255

## Slide 32: Network ID
IP Address: 192.168.0.2  11000000.10101000.00000000.00000010
Subnet Mask: 255.255.255.0  11111111.11111111.11111111.00000000
Network ID: [IP AND Subnet Mask]  192.168.0.0

## Slide 33: Ex1:
IP Address: 192.168.0.3  11000000.10101000.00000000.00000011
Subnet Mask: 255.255.255.0  11111111.11111111.11111111.00000000
Network ID: [IP AND Subnet Mask]  192.168.0.0
Broadcast IP (Directed): convert host part on IP address to 1’s  last 8-bit  192.168.0.255
First Host: Network ID + 1  192.168.0.1
Last Host: Broadcast IP – 1  192.168.0.254

## Slide 34: Ex2:
IP Address: 192.168.3.5/24  11000000.10101000.00000011.00000101
Subnet Mask: 255.255.255.0  11111111.11111111.11111111.00000000
Network ID: [IP AND Subnet Mask]  192.168.3.0
Broadcast IP (Directed): convert host part on IP address to 1’s  last 8-bit  192.168.3.255
First Host: Network ID + 1  192.168.3.1
Last Host: Broadcast IP – 1  192.168.3.254

## Slide 35: Ex3:
IP Address: 192.168.4.129/25  11000000.10101000.00000010.10000001
Subnet Mask: 255.255.255.128  11111111.11111111.11111111.10000000
Network ID: [IP AND Subnet Mask]  192.168.4.128
Broadcast IP (Directed): convert host part on IP address to 1’s  last 8-bit  192.168.4.255
First Host: Network ID + 1  192.168.4.129
Last Host: Broadcast IP – 1  192.168.4.254

## Slide 36: Ex4:
IP Address: 192.168.4.64/26  11000000.10101000.00000010.01000000
Subnet Mask: 255.255.255.192  11111111.11111111.11111111.11000000
Network ID: [IP AND Subnet Mask]  192.168.4.64
Broadcast IP (Directed): convert host part on IP address to 1’s  last 8-bit  192.168.4.127
First Host: Network ID + 1  192.168.4.65
Last Host: Broadcast IP – 1  192.168.4.126

## Slide 37: HW:
IP Address: 192.168.5.33/27  11000000.10101000.00000101.00100001
Subnet Mask: 255.255.255.224  11111111.11111111.11111111.11100000
Network ID: [IP AND Subnet Mask]  192.168.5.32
Broadcast IP (Directed): convert host part on IP address to 1’s  last 8-bit 192.168.5.63
First Host: Network ID + 1  192.168.5.31
Last Host: Broadcast IP – 1  192.168.5.62

## Slide 38: Ex5:
IP Address: 192.168.10.2/25  11000000.10101000.00001010.10000010
Subnet Mask: 255.255.255.128  11111111.11111111.11111111.10000000
Network ID: [IP AND Subnet Mask]  192.168.10.128
Broadcast IP (Directed): convert host part on IP address to 1’s  last 8-bit  192.168.10.255
First Host: Network ID + 1  192.168.10.129
Last Host: Broadcast IP – 1  192.168.10.254

## Slide 39
1) Connection Success
2) Connection fail
3) Connection Success
All PCs have the same Network, same Network ID  192.168.1.0
All PCs have not the same Network, have not same Network ID
Network ID 1  192.168.1.0
Network ID 2  192.168.2.0
[PC can’t connection]
All PCs have the same Network, same Network ID  192.168.0.0
Change subnet mask for all PC to  255.255.0.0

## Slide 40: DHCP Protocol
Dynamic Host Configuration Protocol (DHCP): Application Layer 5
provides services that support network applications. It handles the assignment of IP addresses and network configuration to devices, enabling them to communicate on the network.
Give Host (PC) network configuration :
  IP Address
  Default Gateway
  DNS Server
  Subnet Mask
Automatic Private IP Addressing (APIPA): when there no DHCP Server, PC give itself a network configuration when we choose DHCP.

## Slide 41: DHCP Device?
Switch L2
Router L3
PC L5
Server L5
IP Address
IP Address
Client
DHCP Server
MAC Address
MAC Address
DHCP
Port #
Port #
Data  DORA
D: Discover
O: Offer
R: Request
A: ACK
Data  DORA
D: Discover
O: Offer
R: Request
A: ACK

## Slide 42: DHCP Server
It gives you range of hosts.
It Does not give itself an IP like other PC, you must give it a static IP.
You must not allow to give a Server IP from DHCP server  server must have a constant IP  static IP – manually.
You can put a list of exclusive IPs Address; that DHCP will not give it to any hosts.
IP address of hosts is dynamic  it change in some cases:
  End connection with a network
  Shutdown the host
  Lease time ended

## Slide 43: How it work?
Discover DHCP server (port# 67)  DORA, to get dynamic host configuration network to PC.
DHCP server is a give a Network Services, at main port at server side not client side.
Discover: The client sends out a DHCP Discover message to find available DHCP servers. This is a broadcast message in local network 
IPv4 is Src: 0.0.0.0 & Dest: 255.255.255.255.
MAC is Src: it own MAC & Dest: FF:FF:FF:FF:FF:FF
Q: what is DHCP Relay?
2. Offer: One or more DHCP servers respond with a DHCP Offer message. This message contains an available IP address and other network configuration details.
3. Request: The client responds to the server with a DHCP Request message, indicating that it wants to accept the offered IP address and network configuration.
4. Acknowledgement : The DHCP server sends a DHCP Acknowledge message to confirm that the IP address and network configuration have been assigned to the client. At this point, the client can use the assigned IP address to communicate on the network.

## Slide 44
DHCP Server 2
PC
DHCP Server 1
Discover BC
Discover BC
Request BC
Request BC
Offer
ACK
Offer
Time
Time
Time
Port 68
Port 67
Port 67

## Slide 45
GNS3
GNS3 (Graphical Network Simulator-3)
is a network software emulator that allows users to simulate,
configure, test, and troubleshoot complex networks using virtual devices.

## Slide 46
Wireshark
Wireshark is a popular open-source network protocol analyzer used for capturing and analyzing network traffic in real-time. It helps network administrators and security professionals troubleshoot network issues, monitor network performance, and detect security vulnerabilities.

## Slide 47
ARP example using GNS3
By default, PC is turn Off
You must turn it On

## Slide 48
Open Console in PC

## Slide 49
Start Capture PC wire in Wireshark

## Slide 50
Here we see the capture analysis that we placed on the first computer wire.
First, the device searches for the recipient's MAC address in the ARP table, because for the first time the table is empty, and it will not find the address.
The first message is the ARP message. The device sends a broadcast to all devices asking who owns this IP address, so the receiver sends the MAC address to the sender IP address.
The response is unicast to the sender and contains the recipient MAC address of the message.
The computer saves this address at ARP Table and begins sending the actual message.

## Slide 51
Here is the contents of the first frame sent, the Broadcast frame.
Frame  Physical L1
Ethernet II  Data Link L2
Address Resolution Protocol  message protocol

## Slide 52
- Ethernet II: The frame uses the Ethernet II encapsulation.
- Source: `00:50:79:66:68:00` - The MAC address of the source device sending the frame.
- Destination: `ff:ff:ff:ff:ff:ff` - This indicates a broadcast address, meaning the frame is sent to all devices on the local network.
- Type: `ARP (0x0806)` - The frame contains an ARP (Address Resolution Protocol) packet.
- Padding: `000000000000000000000000000000000000000000` - Additional data added to meet the minimum frame size requirement.
- Frame check sequence (FCS): `0x00000000 [unverified]` - The FCS is used to check the integrity of the frame. Here, it shows as unverified, meaning the checksum has not been validated.
- FCS Status: Unverified - Indicates the frame check sequence status has not been verified.

## Slide 57: Day 3
Outline:
  Transport Layer
  Multiplexing
  Subnetting

## Slide 58: Transport Layer
providing end-to-end communication services for applications. It ensures complete data transfer and manages error correction, data flow, and data segmentation.
Protocols:
  TCP
  UDP
Key Functions:
  Multiplexing and Demultiplexing 
    Allows multiple applications to use the network simultaneously.
    Uses port numbers to direct incoming data
  Segmentation and Reassembly  Data divided & reassembled(TCP)
  Connection Establishment and Termination  connection/less & handshake
  Flow Control  Manages the rate of data transmission (TCP window-based)
  Error Detection and Correction  data integrity (TCP ACK & retransmissions)

## Slide 59: Port
Client: does not provide a service, he uses a random port that is not reserved for a service.
Server: provides services, uses a port designated for this service and continues listening on it (waiting for the client to request the service from this port)
There are three ranges:  []
  Well-Known Ports: 0 – 1023
  Registered Ports: 1024 – 49151
  Dynamic and Private Ports: 49152 – 65535 (Client used).
Note:
The port number is determined in the application layer, and is placed in the control data in the transport layer

## Slide 60: Question
Q: Why is it ineffective to scan all ports by a hacker on a client?
A:
1) There are many ports and checking them all takes a lot of time.
2) When the client requests a service from the server, the random port is opened for a very limited period and then closed again.

## Slide 61
www.bau.edu.jo
Client Side
Application Layer
Transport Layer
Boot Server
443
80
22
21
67
68
51000
50000
443
80
22
21
Listening
HTTP
Data  Request
Segment
src port
51000
dest port
80
Data
Request
Transport
Layer
Application
Layer
Random
24 Hour
www.bau.edu.jo
src port
80
dest port
51000
Data
Page
Transport
Layer
Application
Layer
Request
One page
 Page Response

## Slide 62
www.bau.edu.jo
Client Side
Application Layer
Transport Layer
Server Side
443
80
22
21
67
52000
51000
50000
80
443
22
21
Listening
HTTPS
www.bau.edu.jo
Multiplexing
Request
Multiple pages
www.bau.edu.jo
www.hu.edu.jo
www.bau_students.com
www.bau_students.com
www.hu.edu.jo
Listening
HTTP
Network Layer
One Channel
One Channel
www.bau_students.com
De-Multiplexing
24 Hour
Data  Request
52000
51000
50000
443
80
443
www.bau.edu.jo
50000
443
www.bau_students.com
51000
80

## Slide 63
www.bau.edu.jo
Client Side
Application Layer
Transport Layer
Server Side
443
80
22
21
67
52000
51000
50000
80
22
21
Listening
HTTPS
www.bau.edu.jo
Request
Multiple pages
www.bau_students.com
www.hu.edu.jo
Listening
HTTP
Network Layer
One Channel
One Channel
www.bau_students.com
24 Hour
 Page Response
443
Multiplexing
www.bau.edu.jo
www.bau_students.com
51000
50000
80
443
De-Multiplexing
www.bau.edu.jo
50000
443
www.bau_students.com
51000
80
www.hu.edu.jo
52000
443

## Slide 64
Assembler
Assembly
It takes all instructions and executes them at once.
C Java
Instructions are executed line by line.
Gives direct output per line
CLI Linux MATLAB Python
Interpreter
Compiler

## Slide 65: Basic configuration for Router using CLI
User Model >
Privilege Model #
Configuration Model (config)#
Router Models
Interface level
(config-if)#
Routing engine level
(config-route)#
Line level
(config-line)#
Line level
(dhcp-config)#
enable
disenable
configuration terminal
route rip | ospf…
interface
gigabitEthernet0/0
interface
fastEthernet0/0
line console | vty | tty
ip dhcp pool <name>
show command

## Slide 66: Route Command
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#interface gigabitEthernet0/0
Router(config-if)#ip address 192.168.0.1 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#interface gigabitEthernet0/1
Router(config-if)#ip address 192.168.1.1 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)#do write

## Slide 67: PC in CLI
ipconfig <ip address> <subnet mask> <default gateway>
PC0:
C:\>ipconfig 192.168.0.2 255.255.255.0 192.168.0.1
PC1:
C:\>ipconfig 192.168.1.2 255.255.255.0 192.168.1.1
Ping:
PC0:
ping 192.168.1.2

## Slide 68: DHCP Router
Q: DHCP operates at the Application Layer (Layer 7), and routers are network devices that primarily function at the Network Layer (Layer 3). How can a router also serve as a DHCP server, which is typically a Layer 7 function?
A: Integrated Services: Modern routers often come with integrated software that includes DHCP server functionality. This allows them to manage IP address allocation and network configuration for devices on the network.
DHCP Router
Client
Same Network

## Slide 69
A
B
C

## Slide 70: R1 DHCP Router
R1#configure terminal
R1(config)#interface fastEthernet0/0
R1(config-if)#ip address 192.168.0.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#exit
R1#configure terminal
R1(config)#ip dhcp pool legal
R1(dhcp-config)#network 192.168.0.0 255.255.255.0
R1(dhcp-config)#dns-server 1.1.1.1
R1(dhcp-config)#do write
Building configuration...
[OK]
R2#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
R2(config)#interface fastEthernet0/0
R2(config-if)#ip address dhcp
R2(config-if)#no shutdown
R2(config-if)#exit
R5#show ip interface
FastEthernet0/0 is up, line protocol is up
Internet address is 192.168.0.2/24
Broadcast address is 255.255.255.255
Address determined by DHCP
R2 Client

## Slide 71
Adding Hacker DHCP Router  who will win?
R3#configure terminal
R3(config)#interface fastEthernet0/0
R3(config-if)#ip address 172.16.0.1 255.255.255.0
R3(config-if)#no shutdown
R3(config-if)#exit
R3#configure terminal
R3(config)#ip dhcp pool legal
R3(dhcp-config)#network 172.16.0.0 255.255.255.0
R3(dhcp-config)#dns-server 1.1.1.1
R3(dhcp-config)#do write
Building configuration...
[OK]

## Slide 72
How win? Legal or Hacker

## Slide 73
Random
Hacker
win
Lega
win
Hacker
win

## Slide 74
How can Hacker win?
Winning and losing in this is random.
How can a hacker make his win rate higher than a legitimate router?
The hacker can use some network tactics to increase his chance of winning. For example, he can make the legitimate router busy in other work, such as the hacker sending a DDoS attack on the router.
DDoS
Attack

## Slide 75: SubNetting
Q: Why we need to use subnetting?
Subnetting allows for the creation of multiple subnets, enhancing network organization, management, and security.
Easy to use and manage.

## Slide 76: Ex1:
IP: 192.168.0.4/24
Subnet mask: 255.255.255.0
3 Labs
Subnet mask: 255.255.255.11000000
3 labs  2 Bit needs
IP1: 192.168.0.00000000/26
IP1: 192.168.0.0/26
Subnet mask: 255.255.255.11000000
Network ID: 192.168.0.00000000  0
Broadcast: 192.168.0.00111111  63
IP4: 192.168.0.11000000/26
IP4: 192.168.0.192/26
Subnet mask: 255.255.255.11000000
Network ID:192.168.0.11000000  192
Broadcast: 192.168.0.11111111  225
IP2: 192.168.0.01000000/26
IP2: 192.168.0.64/26
Subnet mask: 255.255.255.11000000
Network ID: 192.168.0.01000000  64
Broadcast: 192.168.0.01111111  127
IP3: 192.168.0.10000000/26
IP3: 192.168.0.128/26
Subnet mask: 255.255.255.11000000
Network ID:192.168.0.10000000  128
Broadcast: 192.168.0.10111111  191

## Slide 77: Ex2:
IP: 192.168.5.0/24
Subnet mask: 255.255.255.0
2 Labs
Subnet mask: 255.255.255.10000000
2 labs  1 Bit need
IP1: 192.168.5.00000000/25
IP1: 192.168.5.0/25
Subnet mask: 255.255.255.10000000
Network ID: 192.168.5.00000000  0
Broadcast: 192.168.5.01111111  127
IP2: 192.168.5.10000000/25
IP2: 192.168.5.128/25
Subnet mask: 255.255.255.10000000
Network ID:192.168.5.10000000  128
Broadcast: 192.168.5.11111111  255

## Slide 78: Ex3:
IP: 192.168.5.0/24
Subnet mask: 255.255.255.0  255.255.255.11100000
7 Labs  3 bits
IP1: 192.168.5.00000000/27
IP1: 192.168.5.0/27
Subnet mask: 255.255.255.11100000
Network ID: 192.168.5.00000000  0
Broadcast: 192.168.5.00011111  31
IP2: 192.168.5.00100000/27
IP2: 192.168.5.32/27
Subnet mask: 255.255.255.11100000
Network ID: 192.168.5.00100000  32
Broadcast: 192.168.5.00111111  63
IP3: 192.168.5.01000000/27
IP3: 192.168.5.64/27
Subnet mask: 255.255.255.11100000
Network ID: 192.168.5.01000000  64
Broadcast: 192.168.5.01011111  95
IP4: 192.168.5.01100000/27
IP4: 192.168.5.96/27
Subnet mask: 255.255.255.11100000
Network ID: 192.168.5.011000000  96
Broadcast: 192.168.5.01111111  127
IP7: 192.168.5.11000000/27
IP7: 192.168.5.192/27
Subnet mask: 255.255.255.11100000
Network ID: 192.168.5.11000000  192
Broadcast: 192.168.5.11011111  223
IP6: 192.168.5.10100000/27
IP6: 192.168.5.160/27
Subnet mask: 255.255.255.11100000
Network ID: 192.168.5.10100000  160
Broadcast: 192.168.5.10111111  191
IP8: 192.168.5.11100000/27
IP8: 192.168.5.224/27
Subnet mask: 255.255.255.11100000
Network ID: 192.168.5.11100000  224
Broadcast: 192.168.5.11111111  255
IP5: 192.168.5.10000000/27
IP5: 192.168.5.128/27
Subnet mask: 255.255.255.11100000
Network ID: 192.168.5.10000000  128
Broadcast: 192.168.5.10011111  159

## Slide 79: Day 4
Outline
  Transport Layer Function
    Segmentation
    Flow Control
    Congestion Control
    Error Detection
  Transport Layer Protocol
    TCP
    UDP
  TCP Session

## Slide 80: Day 4
Outline Continue…
  Router Password
    Enable Password
    Enable Secret
    Console Password
    vty Password
  Telnet in GNS3 & Wireshark
  Public & Private IP
  Application Protocols
  Intro to VLAN

## Slide 81: Transport Layer Function
Multiplexing: combine multiple signals into one medium or channel, from multiple ports coming from Application layer to one channel to Network layer.
Application Layer
Transport Layer
443
80
22
21
67
52000
51000
50000
Multiplexing
www.bau.edu.jo
www.hu.edu.jo
www.bau_students.com
Network Layer
One Channel
52000
51000
50000
443
80
443
50000
51000

## Slide 82: 2. Segmentation (Both)
Dividing data into smaller, more manageable pieces for transmission over a network has several advantages:
Data Integrity: Smaller segments reduce the likelihood of errors.
Error Reduction: Transmitting smaller amounts of data at a time decreases the chances of errors occurring.
Efficient Routing: Each segment can take its own path through the network, depending on traffic conditions.
Reordering by Receiver: The order in which segments are received is not important; the receiver will reorder the segments into the correct sequence, It make at:
  TCP  Transport Layer
  UDP  Application Layer
Application Layer
Transport Layer
50000
Segmentation
Segment 3
Segment 1
Segment 2
50000
50000
50000
443
443
443
Data 5GB

## Slide 83: 3. Flow Control (TCP Only)
manage the rate of data transmission between a sender and a receiver, ensuring that the sender does not overwhelm the receiver with too much data at once.
Problem: If the recipient of the message is slow and cannot receive a large amount of data in a short time, and the sender is fast and can handle a large amount of data by sending and receiving, then the receiver loses some data.
Solution: Before the data is sent, the sender and the receiver agree on the speed of sending the data, depending on how much the slower one can tolerate.
If the route allows more data to be sent, it will be done
Sender
20Mbps
Receiver
5Mbps
Without control flow
20Mbps
15Mbps – size of storage  Loss data
Sender
20Mbps
Receiver
5Mbps
With control flow
5Mbps
Zero Loss data

## Slide 84: 4. Congestion Control (TCP Only)
manage the volume of data being sent into the network to avoid overwhelming it. This involves dynamically by controlling the window size adjusting the rate of data transmission based on current network conditions.

## Slide 85: 5. Error Detection & Correction
Sender
Receiver
TCP
Send Data
If there are error in data, message will be deleted and ask sender to send it again
Sender
Receiver
Send Data Again
Sender
Receiver
Send Data
If there are error in data, message will be deleted only
UDP
Error Correction
Error Detection

## Slide 86: TCP Header
Error Detection
Flow Control
Data Integrity

## Slide 87: UDP Header
Error Detection

## Slide 88
 | TCP | UDP
Connection |  | 
Data Reliable |  | 
Header | big | small
Error Detection |  | 
Error Correction |  | 
Performance |  | 

## Slide 89: Application Layer Protocol  (TCP | UDP)
 | (TCP ¦ UDP)
FTP (20) | TCP
HTTP (80) & HTTPS (443) | TCP
SMTP (25) & POP3 (110) | TCP
Telnet (23) & SSH (22) | TCP
DNS (53) | Primarily UDP for queries, TCP for zone transfers
DHCP (67 (server), 68 (client)) | UDP
TFTP (69) | UDP
ICMP (??) | ??

## Slide 90: Session
Open Session (3-way handshaking) [Hi].
Data Transfer [Data].
Terminate Session (4-way handshaking) [Bye].
TCP/IP  Transport Layer  TCP  Session  Open Session
SYN
  1: Open Session
  0: else
SEQ (Sequence Number)
ensuring data is delivered in the correct order and assists in detecting missing segments.
ACK (Acknowledgment Number)
used by the receiver to indicate the next byte of data it expects to receive from the sender.
Client
BAU Server
SYN=1 SEQ=200
SEQ=201 ACK=401
SYN=1 SEQ=400 ACK=201
Random Port
Port 443
Session opened
Open Session
Data Transferer

## Slide 91: Router Password
Types:
  Enable Password, Secret Password
  Console Password
  Line vty Password
User Model >
Privilege Model #
Configuration Model (config)#
enable
disenable
configuration terminal
Enable password
HTTP
VTY (Remotely  Telnet | SSH)
Console (Physical wire)
Console password
Vty password
1
3
2

## Slide 92: 1. Enable Password
R>enable
R#configure terminal
R(config)#enable password 1234
R(config)#do write
R(config)#exit
R>enable
Password: 1234
R#show run
2. Secret Password
R>enable
R#configure terminal
R(config)#enable secret abcd
R(config)#do write
R(config)#exit
R>enable
Password: 1234
R#show run
Hash Value  MD5

## Slide 93: 3. Console Password
R>enable
R#configure terminal
R(config)#line console 0
R(config-line)#password zinc
R(config-line)#login
R(config-line)#do write
Turn Off Router
Turn On Router
Open Console
Password: zinc
R>
4. vty Password
R>enable
R#configure terminal
R(config)#line vty 0 3
R(config-line)#password zinc
R(config-line)#login
R(config-line)#do write
Turn Off Router
Turn On Router
Open using Telnet | SSH

## Slide 94: VTY Connection Router using Telnet
R>enable
R#configure terminal
R(config)#interface GigaEthernet0/0
R(config)#ip address 192.168.0.1 255.255.255.0
R(config)#no shutdown
R(config)#do ping 192.168.0.2
R(config)#exit
R(config)#line vty 0 4
R(config-vty)#password zinc
R(config-vty)#login
R(config-vty)#exit
R(config)#enable password 1234
R(config)#do write
C:/>telnet 192.168.0.1
Trying ….. Open
Password: zinc
R>enable
Password: 1234
R#

## Slide 95: Secure of VTY Connection in GNS3
R1#conf t
R1(config)#int f0/0
R1(config-if)#ip add 192.168.0.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#exit
IP: 192.168.0.1
SM: 255.255.255.0
IP: 192.168.0.2
SM: 255.255.255.0
R2#conf t
R2(config)#int f0/0
R2(config-if)#ip add 192.168.0.2 255.255.255.0
R2(config-if)#no shutdown
R1(config-if)#exit
F0/0
F0/0

## Slide 96
R1#ping 192.168.0.2
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 192.168.0.2, timeout is 2 seconds:
.!!!!
Success rate is 80 percent (4/5), round-trip min/avg/max = 28/57/80 ms
R1#conf t
R1(config)#enable secret 1234
R1(config)#line vty 0 4
R1(config-line)#password zinc
R1(config-line)#login
R1(config-line)#do wr
R2#telnet 192.168.0.1
Trying 192.168.0.1 ... Open
User Access Verification
Password: <zinc>
R1>en
Password: <1234>
R1#

## Slide 97: Telnet Capture
Q: What can Hacker see?
Q: How is client and how is server?
Q: Telnet Layer?

## Slide 100: Ohhh No…  Hacker See every things

## Slide 101: Private & Public IP Address
Q: why IPv4 still used?
Private & Public IP Address technical
Private IP addresses are used within a private network and are not routable on the internet. They are intended for internal use within an organization or home. (Free)
Public IP addresses are assigned by Internet Service Providers (ISPs) and are routable on the internet. They are unique and must be registered with the Internet Assigned Numbers Authority (IANA). (sale $$)

## Slide 102: NAT (Network Address Translation)
- Routers use NAT to map private IP addresses to a public IP address, allowing multiple devices on a private network to share a single public IP address when accessing the internet.

## Slide 103: Mail Protocols
HW: what difference between SMTP, HTTP, IMAP, and POP3?
HW: FTP use two ports 20 and 21,what are the differences between them?!
HW: what is TFTP Protocol?
Sender
Receiver
Mail Server
Listing for 4 Protocol
SMTP
POP3
IMAP
HTTP

## Slide 104: Ans:
1. SMTP (Simple Mail Transfer Protocol):
Used for sending emails, uses port 25, can also use ports 587 or 465 for encrypted transmission.
Facilitates the sending of email messages between servers. It's used by mail servers to relay outgoing mail.
2. HTTP (Hypertext Transfer Protocol):
Used for transferring hypertext documents, uses port 80 standard 443 for HTTPS secure.
Defines how messages are formatted and transmitted, and how web servers and browsers should respond to various commands. It's the foundation of any data exchange on the Web.
Sender
Mail Server
SMTP
Receiver
Mail Server
HTTP

## Slide 105: Cont…
3. IMAP (Internet Message Access Protocol):
Used for retrieving and storing email on a mail server, port 143 for standard, port 993 for encrypted.
Allows multiple clients to manage and access the same mailbox, providing the ability to view and organize emails on the server.
4. POP3 (Post Office Protocol version 3):
Used for retrieving email from a mail server, port 110 for standard and 995 for encrypted.
Downloads emails from the server to the client and, typically, deletes them from the server afterward. It's designed for users to download their email and then disconnect from the mail server.
Receiver
Mail Server
IMAP
Receiver
Mail Server
POP3

## Slide 106: Subnetting
Problem:
Subnetting & Subnet mask & IP Address in PC Level…
PC know its network.
PC can change its IP Address  sends message to other networks (less secure)
Q: BC message sends to one or different networks?
ARP:
DHCP:
Relay DHCP:

## Slide 107: Broadcast Domain
Same network  End at first router or VLAN.
So VLANs minimize traffic of broadcast.
Without VLANs

## Slide 108: VLAN (L2 Switch)
VLANs (Virtual Local Area Networks) are used to segment the network into different broadcast domains. This helps improve security and performance by isolating network traffic.
At the switching level in the data link layer, it is configured in the switch device.
Users cannot see or change it, and they do not know which VLAN it is in and how many VLANs are in the topology.
If a user changes his IP address, he will not connect to other VLANs.
By default, all devices connected to the switch are in VLAN 1 (the default VLAN), and they are all in the same VLAN.

## Slide 109: Day 5
Outline
  Subnetting & VLANs
    Broadcast in VLANs
    2 VLANs Project
    Switch Ports Modes
      Access Mode
      Trunk
      Dynamic:Auto
      dynamicDesirable
    Intra VLANs
    Router sub-interface & .1q protocol
  Wires
  Project in IntrVLAN
  Routing
  Static VS Dynamic Routing
  Router Simple Project

## Slide 110: Switch Show VLANs
Switch>enable
Switch#show vlan brief
VLAN Name Status Ports
---- -------------------------------- --------- -------------------------------
1 default active Fa0/1, Fa0/2, Fa0/3, Fa0/4
Fa0/5, Fa0/6, Fa0/7, Fa0/8
Fa0/9, Fa0/10, Fa0/11, Fa0/12
Fa0/13, Fa0/14, Fa0/15, Fa0/16
Fa0/17, Fa0/18, Fa0/19, Fa0/20
Fa0/21, Fa0/22, Fa0/23, Fa0/24
Gig0/1, Gig0/2
1002 fddi-default active
1003 token-ring-default active
1004 fddinet-default active
1005 trnet-default active

## Slide 111: Example 1
.2
.5
.4
.3
All same Network: 192.168.0

## Slide 112: Example 1
Switch#configure terminal
Switch(config)#vlan 2
Switch(config-vlan)#exit
Switch(config)#vlan 3
Switch(config-vlan)#exit
Switch(config)#interface fastEthernet0/1
Switch(config-if)#switchport mode access
Switch(config-if)#switchport access vlan 2
Switch(config-if)#do write
Switch(config-if)#exit
Switch(config)#interface fastEthernet0/2
Switch(config-if)#switchport mode access
Switch(config-if)#switchport access vlan 2
Switch(config-if)#do write
Create VLAN 2
Put VLAN 2 in port f0/1 & select mode
Put VLAN 2 in port f0/2 & select mode
Create VLAN 3

## Slide 113: Example 1
Switch(config)#interface fastEthernet0/3
Switch(config-if)#switchport mode access
Switch(config-if)#switchport access vlan 3
Switch(config-if)#do write
Switch(config-if)#exit
Switch(config)#interface fastEthernet0/4
Switch(config-if)#switchport mode access
Switch(config-if)#switchport access vlan 3
Switch(config-if)#do write
Put VLAN 3 in port f0/3 & select mode
Put VLAN 3 in port f0/4 & select mode

## Slide 114: Switch Show VLANs
Switch#show vlan brief
VLAN Name Status Ports
---- -------------------------------- --------- -------------------------------
1 default active Fa0/5, Fa0/6, Fa0/7, Fa0/8
Fa0/9, Fa0/10, Fa0/11, Fa0/12
Fa0/13, Fa0/14, Fa0/15, Fa0/16
Fa0/17, Fa0/18, Fa0/19, Fa0/20
Fa0/21, Fa0/22, Fa0/23, Fa0/24
Gig0/1, Gig0/2
2 VLAN0002 active Fa0/1, Fa0/2
3 VLAN0003 active Fa0/3, Fa0/4
1002 fddi-default active
1003 token-ring-default active
1004 fddinet-default active
1005 trnet-default active

## Slide 115: Connection
Network | VLAN | Connection
Same | Same | 
Same | Different | 
Different | Same | 
Different | Different | 

## Slide 116: Example 2

## Slide 117: Switch Port Models
Switch ports can be configured in different modes:
Access Mode:
is a port configuration mode used on switches for connecting end devices such as computers, printers, and servers.
The port is assigned to a single VLAN.
All traffic coming in and out of the port is untagged, meaning that VLAN information is not included in the Ethernet frames.
Devices connected to an access port are unaware of VLANs.
.2
.5
.4
.3

## Slide 118: Access Mode Used
.2
.3
.4
.5
v2
v3
v3
v2
.2
.3
.4
.5
v2
v3
v3
v2
.2
.3
.4
.5
v2
v3
v3
v2
.2
.3
.4
.5
v2
v3
v3
v2
NID: 192.168.0
SM: /24
??
??

## Slide 119: Problem
Sender
.5
.4
.3
.2
Receiver
v3
v2
v3
v2
Sender
.5
.4
.3
.2
Receiver
v3
v2
v3
v2
Sender
.5
.4
.3
.2
Receiver
v3
v2
v3
v2
Sender
.5
.4
.3
.2
Receiver
v3
v2
v3
v2
??
v1
v1
v1
v1

## Slide 120: 2. Trunk Mode
is used on switch ports to carry traffic for multiple VLANs used between routers and servers.
can carry traffic from multiple VLANs.
Traffic on a trunk port is tagged with VLAN identifiers (DTP).
A trunk port can have a native VLAN, which is the VLAN for untagged traffic. By default, the native VLAN is VLAN 1.
Q: Native VLAN?
.2
.5
.4
.3

## Slide 121: Use Trunk
Sender
.5
.4
.3
.2
Receiver
v3
v2
v3
v2
Sender
.5
.4
.3
.2
Receiver
v3
v2
v3
v2
Sender
.5
.4
.3
.2
Receiver
v3
v2
v3
v2
Sender
.5
.4
.3
.2
Receiver
v3
v2
v3
v2
??
Message Deleted
VLAN 2
??
Access
Access
Trunk
Trunk

## Slide 122: Dynamic Mode (Auto and Desirable Modes)
DTP is a Cisco proprietary protocol that negotiates trunking on a link between two devices and helps manage the trunk links dynamically.
 | Access | Trunk | Auto | Desirable
Access | A |  | A | A
Trunk |  | T | T | T
Auto | A | T | A | T
Desirable | A | T | T | T

## Slide 123: Dynamic Trunking Protocol (1. Access)
A
A
A
A
1
A
T
A
T
2
A
Auto
A
A
3
A
D
A
A
4

## Slide 124: Dynamic Trunking Protocol (2. Trunk)
T
T
T
T
5
T
A
T
A
6
T
Auto
T
T
7
T
D
T
T
8

## Slide 125: Dynamic Trunking Protocol (3. Auto)
Auto
T
T
T
5
Auto
A
A
A
6
Auto
Auto
A
A
7
Auto
D
T
T
8

## Slide 126: Dynamic Trunking Protocol (4. Desirable)
T
T
T
5
D
A
A
A
6
D
Auto
T
T
7
D
D
T
T
8
D

## Slide 127: Hacker
Hacker Kali PC
Using virtual Switch
Main Switch
Trunk
Trunk
Auto
Desirable
Can Access to all network if main Switch in at
Truck or Auto or Desirable.

## Slide 128: Problem
If we need to connected between to VLANs, we need to use Router.
Problems:
Router can not work with Trunk Mode (Header of message will change so router will delete the message, he think it wrong message because the CRC | FSC flag will change in Trunk Mode  Because we add the VLAN Tag).
For each VLAN we need to add a new Interface in the router (so expensive).
When message get out of router it will not get a VLAN Tag, because router do not work with Trunk Mode.

## Slide 130: Inter VLAN
allows communication between different VLANs.
We need to use it with Sub-Interface:
A sub-interface in a router is a logical interface created within a physical interface.
Allowing multiple VLANs to share a single physical interface while remaining logically separated.
Dot1Q:
protocol is a networking standard that supports VLANs (Virtual Local Area Networks) on an IEEE 802.3 (Ethernet) network.
When a frame enters a VLAN-aware switch or router, the device adds an 802.1Q tag to the frame header if it is to be sent out on a trunk link.
G0/0
G0/0.1
G0/0.2
Trunk
Dot1Q
A
A

## Slide 131: Wire
Straight-through Ethernet Cable:
used to connect different types of devices. It has the same wiring standard on both ends.
Uses:
  Connecting a computer to a switch or hub
  Connecting a router to a modem
  Connecting different network devices to a central networking device
Crossover Ethernet Cable:
used to connect similar types of devices directly, without the need for a switch or hub. The internal wiring swaps the transmit and receive signal pairs, allowing two devices to communicate directly.
Uses
  Connecting two computers directly
  Connecting two switches directly
  Connecting two routers directly
L2
L3 or more
L3 or more
L3 or more
L2
L2

## Slide 132: IntrVLAN Example
Switch(config)#int f0/1
Switch(config-if)#switchport mode access
Switch(config-if)#switchport access vlan 2
% Access VLAN does not exist. Creating vlan 2
Switch(config-if)#exit
Switch(config)#int f0/2
Switch(config-if)#switchport mode access
Switch(config-if)#switchport access vlan 3
% Access VLAN does not exist. Creating vlan 3
Switch(config-if)#exit
Switch(config)#int g0/1
Switch(config-if)#switchport mode trunk
Switch(config-if)#do write
Building configuration...
[OK]
GW: 192.168.0.1
GW: 192.168.1.1
VLAN 2
VLAN 3
Trunk

## Slide 133
Router>en
Router#conf t
Router(config)#int g0/0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#int g0/0.1
Router(config-subif)#encapsulation dot1Q 2
Router(config-subif)#ip address 192.168.0.1 255.255.255.0
Router(config-subif)#exit
Router(config)#int g0/0.2
Router(config-subif)#encapsulation dot1Q 3
Router(config-subif)#ip address 192.168.1.1 255.255.255.0
Router(config-subif)#do wr
Building configuration...
[OK]

## Slide 134: Routing
From router to router, or from interface to interface
Router Function:
  Connection between different networks or VLANs.
  Choose the best path (Manually or Dynamically)
  DHCP, Telnet, and ping & so on
Se0/0
Se0/1

## Slide 135
Sender
Receiver
3
1
2

## Slide 136
Sender
Receiver
3
1
2

## Slide 137: Static VS Dynamic Routing
 | Static | Dynamic
Security |  | 
Performance (Speed) |  | 
Availability (Always On) |  | 
Ease of Configuration |  | 
Used | Small network & Secure | Large network

## Slide 138: Static Routing Example
Router do not need a manual configuration if there are only one router.
Because it have a Routing Table.
Network ID | Interface
192.168.0.0 | G0/0
192.168.1.0 | G0/1
Router Table

## Slide 139: What Happens?
RT = IP AND SM
No configurations are placed on the router, it is completely automatic.
When the message reaches the router, it sends it to the receiving network automatically, how does this happen?
The router contains a table called the router table, which contains the Network ID and the interface associated with it.
Network ID | Interface
--------------------------------
192.168.0.0 | G0/0
192.168.1.0 | G0/1
When the message reaches the router, it does an ending between the dest IP address and the dest subnet mask.
Dest IP = 192.168.1.2
Dest SM = 255.255.255.0
Dest NID = 192.168.1.0
So… From Routing Table:
Int = G0/1

## Slide 140: CLI
Router>en
Router#conf t
Router(config)#int g0/0
Router(config-if)#no shutdown
Router(config-if)#ip address 192.168.0.1 255.255.255.0
Router(config-if)#exit
Router(config)#int g0/1
Router(config-if)#no shutdown
Router(config-if)#ip address 192.168.1.1 255.255.255.0
Router(config-if)#do wr
Router(config-if)#exit

## Slide 141: Routing Table

## Slide 142: Direct Connect
connecting two or more routers directly without the need for intermediary devices or networks.
Direct connection is directly from the router to the next router, no matter how many switches are between them

## Slide 143: Day 6
Outline
  Static Routing Example
  Dynamic Routing (OSPF)
    Area
    Area Border Router
    OSPF Projects
    GNS3 Project
  Router RAM, Flash, and NVRAM
  Configuration Register (Rommon)

## Slide 144: Static Routing Example

## Slide 145: CLI
Router>en
Router#conf t
Router(config)#int g0/0
Router(config-if)#no shutdown
Router(config-if)#ip address 192.168.0.1 255.255.255.0
Router(config-if)#exit
Router(config)#int g0/1
Router(config-if)#no shutdown
Router(config-if)#ip address 192.168.2.1 255.255.255.0
Router(config-if)#do wr
Router(config-if)#exit
Router1>en
Router1#conf t
Router1(config)#int g0/0
Router1(config-if)#no shutdown
Router1(config-if)#ip address 192.168.1.1 255.255.255.0
Router1(config-if)#exit
Router1(config)#int g0/1
Router1(config-if)#no shutdown
Router1(config-if)#ip address 192.168.2.2 255.255.255.0
Router1(config-if)#do wr
Router1(config-if)#exit
Q: Is that enough to do ping?

## Slide 146: No Connection…
Network ID | Interface
192.168.0.0 | G0/0
192.168.2.0 | G0/1
R0 Router Table
Network ID | Interface
192.168.1.0 | G0/0
192.168.2.0 | G0/1
R1 Router Table
Src IP | Dest IP | Data
192.168.0.2/24 | 192.168.1.2/24 | Hi
When this message reaches the router, it finds that the receiving network is not in the table!!!
Dest IP = 192.168.1.2
Dest SM = 255.255.255.0
Dest NID = 192.168.1.0
 Dest Int = ?? Not found in R0 RT

## Slide 147: Reply From the gateway…
The interface sends a message to the sender that it did not find the requested network.
Type of response:
  Reply TTL (successfully connection)
  Reply From Router Interface (dest NID is not found)
  Request Time Out

## Slide 148: How do we solve this problem?
Now we just need to tell the first router (R0) that there is a network ID(192.168.1.0) and its interface is (G0/1), how do we do that?
Static Way…

## Slide 150: Will the devices communicate now?

## Slide 151: Why request time out?
After the message was sent from the Sender PC, it arrived correctly to the Receiver PC, and when the receiver PC sent the reply message, the second router (R1) could not find the 192.168.0.0 network, so no reply reached the sender PC.

## Slide 153: Ping Scanner
Searching for TTL after pinging devices
TTL is only present when the connection is successful
If the connection is not successful or there is no response, this does not mean that the device is not present, this may be due to the work of the firewall, which in many cases prevents the response of messages to increase security

## Slide 154: Routing
Routing in a network involves determining the paths for data packets to travel from a source to a destination.
Static Routing: involves manually configuring the routes in a network. This means that the network administrator specifies the paths that data packets should take to reach their destinations.
Advantages:
1. Simplicity: straightforward to implement in small networks.
2. Predictability: The path that packets will take is predictable and consistent.
3. Security: Less risk of routing loops or malicious route alterations.
4. Low Overhead: Reducing network overhead.
Disadvantages:
1. Lack of Scalability: Managing static routes becomes impractical in large, complex networks.
2. No Automatic Failover: If a route becomes unavailable, there is no automatic rerouting, which can lead to network downtime.

## Slide 155: Dynamic Routing
involves using routing protocols to automatically discover and maintain the routes within a network. Routers exchange routing information and update their routing tables dynamically as the network topology changes.
Advantages:
1. Scalability: suitable for large and complex networks with many routers and paths.
2. Automatic Failover: can detect changes in the network and reroute traffic automatically, enhancing network reliability and availability.
3. Ease of Maintenance: requires less manual intervention compared to static routing.
4. Adaptability: can adapt to changes in network topology, such as adding or removing routers and links.

## Slide 156: Cont…
Disadvantages:
1. Complexity: more complex to configure and manage compared to static routing.
2. Resource Consumption: consume more CPU, memory, and bandwidth due to routing updates and calculations.
3. Potential for Routing Loops: can lead to routing loops and suboptimal routing.
Use Cases:
- Large Enterprise Networks: is ideal for large enterprises with multiple subnets and complex topologies.
- Service Provider Networks: are commonly used by service providers to manage the routing of large-scale networks.
- Highly Available Networks: Networks that require high availability and automatic failover benefit from dynamic routing.

## Slide 157: OSPF (Open Shortest Path First)
is a dynamic routing protocol used in Internet Protocol (IP) networks.
Shortest Path First Algorithm: OSPF uses Dijkstra's algorithm to calculate the shortest path tree for each route, ensuring efficient and optimal path selection.
Neighbor Discovery: OSPF routers discover other OSPF routers on their directly connected networks using Hello packets. Routers become neighbors if they agree on certain parameters.

## Slide 158: Cost
F: Fiber = 10
F: Fiber = 10
F: Fiber = 10
GE: Giga Ethernet = 100
FE: Fast Ethernet = 200
M: Microsoft = 350

## Slide 159: OSPF Steps
Connection Router
Dijkstra's algorithm
Router Table
Startup

## Slide 160: OSPF Area
An OSPF area is a logical grouping of OSPF routers that helps manage routing by dividing a large network into smaller, more manageable segments. Each OSPF area maintains its own link-state database (LSDB) and limits the scope of LSAs (Link-State Advertisements) to reduce overhead and improve performance.

## Slide 161: ABR Router
1. Internal Router: A router with all interfaces within the same OSPF area.
2. Area Border Router (ABR): Connects two or more OSPF areas, maintaining separate LSDBs for each area and propagating routing information between them.
ABR Router
Area 0
Area 1
Area 0
Area 1

## Slide 162: Dynamic Routing Example 1

## Slide 163: CLI
Router>en
Router#conf t
Router(config)#int g0/0
Router(config-if)#no shutdown
Router(config-if)#ip address 192.168.0.1 255.255.255.0
Router(config-if)#exit
Router(config)#int g0/1
Router(config-if)#no shutdown
Router(config-if)#ip address 192.168.2.1 255.255.255.0
Router(config-if)#do wr
Router(config-if)#exit
Router1>en
Router1#conf t
Router1(config)#int g0/0
Router1(config-if)#no shutdown
Router1(config-if)#ip address 192.168.1.1 255.255.255.0
Router1(config-if)#exit
Router1(config)#int g0/1
Router1(config-if)#no shutdown
Router1(config-if)#ip address 192.168.2.2 255.255.255.0
Router1(config-if)#do wr
Router1(config-if)#exit
Q: Is that enough to do ping?

## Slide 164
This is the same example we used before, and we solve it using Static Routing.
How to solve it now using Dynamic Routing  OSPF Protocol??
Router(config)#route ospf 1
Router(config-route)# network 192.168.0.0 0.0.0.255 area 0
Router(config-route)# network 192.168.1.0 0.0.0.255 area 0
Router1(config)#route ospf 1
Router1(config-route)# network 192.168.2.0 0.0.0.255 area 0
Router1(config-route)# network 192.168.1.0 0.0.0.255 area 0

## Slide 165: Dynamic Routing Example 2

## Slide 166
Router1(config)#route ospf 1
Router1(config-route)# network 192.168.1.0 0.0.0.255 area 0
Router1(config-route)# network 192.168.2.0 0.0.0.255 area 0
Router1(config-route)# network 192.168.4.0 0.0.0.255 area 1
Router2(config)#route ospf 1
Router2(config-route)# network 192.168.4.0 0.0.0.255 area 1
Router2(config-route)# network 192.168.3.0 0.0.0.255 area 1
Router0(config)#route ospf 1
Router0(config-route)# network 192.168.0.0 0.0.0.255 area 0
Router0(config-route)# network 192.168.2.0 0.0.0.255 area 0
Area 0
Area 1

## Slide 167: GNS3 Example

## Slide 170: Message

## Slide 171: Broadcast
Broadcasting involves sending a data packet from one sender to all possible recipients within a network segment.
Characteristics:
- One-to-All: The sender transmits the data to all devices on the network.
- No Specific Target: Every device on the network segment receives the broadcast packet.
- Network Flooding: Broadcast traffic can cause network congestion if used excessively.
Use Cases:
- ARP Requests: Used to discover the MAC address corresponding to an IP address.
- DHCP Discovery: Used by a client to find available DHCP servers on the network.
- Routing Protocol Updates: Some protocols use broadcasts to distribute routing information.

## Slide 172: Uni-cast
Unicasting involves sending a data packet from one sender to a specific recipient.
Characteristics:
- One-to-One: The sender transmits the data to a single, specific recipient.
- Direct Communication: Only the intended recipient processes the unicast packet.
- Efficient Use of Bandwidth: No unnecessary data transmission to other devices.
Use Cases:
- Standard Network Communication: Most internet traffic (e.g., web browsing, file transfers) is unicast.
- Email: Sending an email from one user to another.

## Slide 173: Multicast
Multicasting involves sending a data packet from one sender to multiple specific recipients, typically belonging to a multicast group.
Characteristics:
- One-to-Many: The sender transmits the data to multiple recipients that are part of a multicast group.
- Efficient Distribution: Data is only sent to devices that have joined the multicast group, reducing unnecessary traffic.
- Requires Support: Network infrastructure and devices must support multicast to handle it properly.

## Slide 174
RAM
OS Config
Flash
OS
IOS (without configuration)
NVRAM
OS Configuration:
- password
IP Address
OSPF
Hostname
No shutdown
Startup Config
Running Config
copy startup-config running-config
copy running-config startup-config  do write

## Slide 175: Configuration Register
Configuration Register Bits Breakdown
Bits 0-3: Boot Field
  0x0: Manual boot (ROM Monitor mode)
  0x1: Boot to the first image in the flash
  0x2-F: Specifies a specific image to boot
Bits 6-7: Console Speed
  00: 9600 bps (default)
  01: 4800 bps
  10: 2400 bps
  11: 1200 bps
Bit 8: Break Enable/Disable
  0: Break disabled (default)
  1: Break enabled
Bit 10: Ignore NVRAM
  0: Use startup-config (default)
  1: Ignore startup-config (useful for password recovery)

## Slide 176: Configuration Register 0x2102
0x2102 is the default configuration register setting for most Cisco routers.
Boot Normally: Load the IOS from flash memory.
Use NVRAM: Read the startup configuration file (usually located in NVRAM) to configure the router.
Baud Rate: Uses the default console baud rate of 9600 bps.

## Slide 177: Configuration Register 0x2142
Ignore NVRAM: During boot, the router ignores the startup configuration file in NVRAM. This allows the router to boot without applying the saved configuration.
This setting is primarily used for:
Password Recovery: When an administrator has forgotten the enable password or other critical access passwords.
Troubleshooting: If a faulty configuration is preventing the router from booting correctly, ignoring the startup configuration allows for troubleshooting and correcting the issue without applying the problematic configuration.

## Slide 179
Ctrl + C
Router  Power Off
Router  Power On

## Slide 180
Router#copy startup-config running-config
Destination filename [running-config]?
720 bytes copied in 0.416 secs (1730 bytes/sec)
NAme_Royte_1#
%SYS-5-CONFIG_I: Configured from console by console
NAme_Royte_1#conf t
NAme_Royte_1(config)#enable password 1234
NAme_Royte_1(config)#do wr
Building configuration...
[OK]
NAme_Royte_1(config)#config-register 0x2102

## Slide 181: Day 7
Outline
  Network Exam
  Network Design Structure
    Core Layer
    Distribution Layer
    Access Layer
    Small LAN
    Labs
    Manager PC
    Data center

## Slide 182: Cont…
Outline
  Servers
    Web Server
    DNS Server
    DHCP Server
    Mail Server
    Log Server
    Authentication Server
    TACACS Server
    Radius Server
    Kerberos Server
  Internal Hacker VS External Hacker

## Slide 185: Network Design Structure
Designing a network involves several considerations, including the size and purpose of the network, the types of devices, and the required security measures.
1. Core Layer
The backbone of the network, providing high-speed, highly reliable connectivity between different parts of the network.
- Devices: High-performance routers and switches.
- Characteristics: High-speed data transfer, redundancy, fault tolerance.

## Slide 186: 2. Distribution Layer
Aggregates data from the access layer switches and forwards it to the core layer. It also provides policy-based connectivity, such as routing, filtering, and QoS (Quality of Service).
- Devices: Layer 3 switches (switches with routing capabilities).
- Characteristics: Scalability, security policies, routing between VLANs (Virtual Local Area Networks).

## Slide 187: 3. Access Layer
Connects end devices like PCs, printers, and IP phones to the network. It also manages user access to the network.
- Devices: Layer 2 switches.
- Characteristics: Port density, PoE (Power over Ethernet) for IP phones and wireless access points, VLAN segmentation.

## Slide 188: Cont…
Small LAN: Provides network connectivity within a small office or a small department.
Labs: Provide network connectivity for lab environments where testing, development, and research take place.
Manager PCs: Provide network connectivity for managers, ensuring they have high-priority access to network resources.

## Slide 189: Key Considerations
1. Scalability: Ensure the network can grow with the organization's needs.
2. Redundancy: Implement redundant paths and devices to ensure network availability.
3. Security: Use firewalls, access control lists (ACLs), and VLANs to segment and secure the network.
4. Performance: Implement QoS to prioritize critical traffic, ensure sufficient bandwidth, and minimize latency.
5. Manageability: Use centralized management tools to monitor and configure network devices.

## Slide 190: Data center
A data center is a facility composed of networked computers and storage that businesses or other organizations use to organize, process, store, and disseminate large amounts of data
Servers
Storage Systems
Networking Equipment
Power Supply
Cooling Systems

## Slide 191: Servers
DNS Server: Translates domain names (e.g., www.example.com) into IP addresses (e.g., 192.168.1.1), allowing users to access websites using human-readable names.
Web Server: Serves web pages to users over the internet or an intranet. It handles HTTP or HTTPS requests from clients (browsers) and delivers the corresponding web pages.
DHCP Server: Automatically assigns IP addresses and other network configuration parameters to devices on a network
Mail Server: Handles the sending, receiving, and storage of email messages. It includes both SMTP for sending emails and POP3/IMAP for retrieving emails.

## Slide 192
1
4
3
2
Name
Name
Search in DNS Table
-------------------------
Name | IP Address
IP Address
IP Address
DNS Server

## Slide 193
5
8
7
6
Web Server

## Slide 194
DHCP Server 2
PC
DHCP Server 1
Discover BC
Discover BC
Request BC
Request BC
Offer
ACK
Offer
Time
Time
Time
Port 68
Port 67
Port 67
DHCP Server

## Slide 195: Mail Server
Sender
Receiver
Mail Server
Listing for 4 Protocol
SMTP
POP3
IMAP
HTTP

## Slide 196: Log Server
Log Server: Collects, stores, and manages log data from various network devices, servers, applications, and other systems.
- Enables centralized logging for monitoring, troubleshooting, and auditing purposes.
- Syslog: A standard protocol for logging.
- Elasticsearch, Logstash, Kibana (ELK Stack): A popular open-source stack for searching, analyzing, and visualizing log data.
- Splunk: A comprehensive platform for operational intelligence and log management.
- Graylog: An open-source log management solution.

## Slide 197: Authentication Server
Authentication Server: - Verifies the identity of users and devices attempting to access network resources.
- Manages user credentials and access policies.
- Directory Services: Databases that store user information and credentials.
- Authentication Protocols: Mechanisms like LDAP, Kerberos, and OAuth that handle the authentication process.
- Access Control Policies: Rules that define what resources authenticated users can access.
- Microsoft Active Directory (AD): A directory service for Windows domain networks.

## Slide 198: TACACS Server
TACACS Server (Terminal Access Controller Access-Control System): Provides centralized authentication, authorization, and accounting (AAA) for users accessing network devices.
- Often used for administrative access to routers, switches, and other network infrastructure.
- Authentication: Verifies user credentials.
- Authorization: Determines user permissions for accessing specific network resources.
- Accounting: Tracks user activities and sessions.
- Cisco Secure ACS (Access Control Server): A server for managing AAA services.
- FreeRADIUS: An open-source RADIUS server with TACACS+ support.

## Slide 199: Radius Server
Radius Server: Provides AAA services for users connecting to a network, particularly for remote access.
- Authenticates users, authorizes their access, and logs their activities.
- FreeRADIUS: A widely used open-source RADIUS server.
- Microsoft NPS (Network Policy Server): A RADIUS server and proxy in Windows Server.
- Cisco ISE (Identity Services Engine): Provides RADIUS services along with advanced identity management.

## Slide 200: Kerberos Server
Kerberos Server: Provides secure authentication using secret-key cryptography.
- Issues tickets for proving identity within a network.
- Key Distribution Center (KDC): The core component that includes:
  - Authentication Server (AS): Authenticates users and issues Ticket Granting Tickets (TGT).
  - Ticket Granting Server (TGS): Issues service tickets based on the TGT.
- Tickets: Encrypted tokens used for authenticating users to services.

## Slide 201: Internal Hacker VS External Hacker
 | Internal Hacker | External Hacker
Access Level | Already has authorized access | No authorized access, must breach defenses
Knowledge | Familiar with internal systems and policies | Limited or no knowledge, must conduct reconnaissance
Motivations | Financial gain, revenge, ideology, negligence | Financial gain, political/ideological, reputation, espionage
Prevention | Access controls, monitoring, security training | Firewalls, IDS, regular patching, MFA

## Slide 202: Thank You